## Slide 1
Schuylkill Valley School District
District-Wide Feasibility Study
7 March 2020

## Slide 2
Schuylkill Valley SD Feasibility Study
Project Team
Schuylkill Valley School District
Owner
EI Associates
Architects & Educational Facilities Planners
K&W
Civil / Site Engineering
SitelogiQ (formerly Reynolds)
Mechanical, Electrical, Plumbing Engineering / Estimates
Advanced Foodservice Solutions
Food Service / Kitchen Design
Baker, Ingram & Associates
Structural Engineering

## Slide 3
Schuylkill Valley SD Feasibility Study
Process / Contents of the Study
Demographic Review
(Student Enrollment, Population, Housing)
Facilities Study (Building Improvements & Construction Cost)
Educational Program Review
(Requirements / Needs)
Solutions (Construction Options)
Cost of Options
Schedule
Note: Study per PDE Requirements

## Slide 4
Schuylkill Valley SD Feasibility Study
Demographic Exploration - Population
2000 - 2010
Gain of Population
+ 1046
2010 - 2017
Gain of Population
+ 772
2000 - 2017
Gain of Population
+ 1818

## Slide 5
Schuylkill Valley SD Feasibility Study
Demographic Exploration - Housing
2000 - 2010
Gain of Housing
+ 575
2010 - 2017
Gain of Housing
+ 108
2000 - 2017
Gain of Housing
+ 683

## Slide 6
Schuylkill Valley SD Feasibility Study
Demographic Exploration – Historical Student Enrollment
2000 - 2010
Gain of Students
+ 58
2010 - 2017
Gain of Students
+ 117
2000 - 2017
Gain of Students
+ 175

## Slide 7
Architects, Civil and MEP Engineers, and Kitchen Designers survey buildings and sites
  Security
  Safety
  Codes
  Condition
  Mechanical
  Electrical
  Plumbing
  Site
PHYSICAL PLANT
EDUCATIONAL PROGRAMMING
  Efficient Program-Use of Facilities
  Size / Future Capacity of Schools
  Grade Realignment / Grade Levels
  Students per Classroom
  Use of Core Facilities
  Site – Parking, Drives, Playfields
Facilities Evaluation Process
Improvement Lists: Itemized, Priced, and Prioritized

## Slide 8
  Estimates = 1 year window
Facilities Evaluation Process
Improvement Lists: Itemized, Priced, and Prioritized
ITEMIZED ESTIMATED COSTS
Architects, Civil and MEP Engineers, and Kitchen Designers estimate costs for each work item individually

## Slide 9
Architect, Engineers, and SD Team prioritize the work items and assign ranking to each work item
RANK 1
HIGH PRIORITY
RANK 2
MEDIUM PRIORITY
RANK 3
LOW PRIORITY
FUTURE CONSIDERATION
RANK 4
OPTIONAL
SEPARATE FUTURE PROJECTS
Facilities Evaluation Process
Improvement Lists: Itemized, Priced, and Prioritized

## Slide 10
Schuylkill Valley Elementary School
Existing Conditions
FACILITIES IMPROVEMENTS:
Overall Campus Site Improvement
Roof Rehabilitation / Repair
Energy Efficient Doors & Windows
Interior Finishes
Casework Replacement
Kitchen Equipment Upgrades
MEP Replacement
Safety / Security Upgrades
Building Code Upgrades
Accessibility Upgrades
Fire Protection System Install
Grades K-4
Built: 1993
Site: 110.41 acres*
Area: 112,000 SF
District Capacity: 792
2019-20 Enrollment: 791
FIRST FLOOR
SECOND FLOOR

## Slide 11
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
Elementary School

## Slide 12
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
Elementary School

## Slide 13
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
Elementary School
Lighting Levels – Foot-Candles
Room # | Space Type | Sound Level (dB)
B204 | Classroom - General | 43.9
B104 | Classroom - General | 0.0
Library | Library - Reading/Studying | 44.6
Sound Levels

## Slide 14
Schuylkill Valley Middle School
Existing Conditions
Built: 1974(B), 1998(A), 2007(A&A)
Site: 110.41 acres*
Area: 152,000 SF
District Capacity: 718
2019-20 Enrollment: 684
Grades 5-8
SECOND FLOOR
FIRST FLOOR
FACILITIES IMPROVEMENTS:
Overall Campus Site Improvement
Roof Rehabilitation / Repair
Exterior Wall Repair / Cleaning
Limited Interior Finishes Upgrades
Limited Interior Acoustic Improvement
Limited MEP Upgrades
Building Code Upgrades
Accessibility Upgrades

## Slide 15
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
Middle School

## Slide 16
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
Middle School

## Slide 17
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
Middle School
Lighting Levels – Foot-Candles
Room # | Space Type | Sound Level (dB)
D109 | Classroom - General | 52.6
C208 | Classroom - General | 0.0
A219 | Classroom - General | 50.3
Library | Library - Reading/Studying | 42.1
Sound Levels

## Slide 18
Schuylkill Valley High School / DAO
Existing Conditions
Grades 9-12
Built: 1959(B), 1995(A&A) 2000(DAO, A&A), 2006(A&A)
Site: 110.41 acres*
Area: 182,000 SF (with DAO)
District Capacity: 752
2019-20 Enrollment: 636
SECOND FLOOR
FIRST FLOOR
FACILITIES IMPROVEMENTS:
Overall Campus Site Improvement
Roof Rehabilitation / Repair
Exterior Wall Repair / Cleaning
Limited Interior Finishes Upgrades
Limited Interior Acoustic Improvement
MEP Upgrades
Building Code Upgrades
Accessibility Upgrades

## Slide 19
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
High School

## Slide 20
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
High School

## Slide 21
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
High School

## Slide 22
Schuylkill Valley SD Feasibility Study
Existing Conditions – MEP
High School
Lighting Levels – Foot-Candles
Room # | Space Type | Sound Level (dB)
D31 | Classroom - General | 42.5
C-26 | Classroom - General | 48.1
F-105 | Classroom - General | 44.5
Library | Library - Reading/Studying | 51.3
Weight Room | Gymnasium - General Exercise | 49.8
Sound Levels

## Slide 23
Schuylkill Valley School District
Summary - Building Improvement Construction Costs
Elementary School

## Slide 24
Schuylkill Valley School District
Summary - Building Improvement Construction Costs
Middle School

## Slide 25
Schuylkill Valley School District
Summary - Building Improvement Construction Costs
High School

## Slide 26
EDUCATIONAL PROGRAM IMPROVEMENTS:
(2) Additional Graded Classrooms per Grade K-4
Additional Support Classrooms
(5) Additional Divided Support Classrooms (1 per Grade)
Additional S.E. Seminar Room / S.G.I.
Additional Art Classroom
Add Auxiliary Gymnasium
Enlarged Student Dining
Enlarged Kitchen Area
Enlarged Administration Office
Additional Faculty Room / I.P.C.
Additional Faculty Dining / Work Room
Schuylkill Valley Elementary School
Existing Conditions

## Slide 27
Schuylkill Valley Middle School
Existing Conditions
EDUCATIONAL PROGRAM IMPROVEMENTS:
(2) Additional Graded Classrooms per Grade 5-8
Additional Support Classroom
(4) Additional Divided Support Classrooms (1 per Grade)
Additional S.E. Seminar Room / S.G.I.
Enlarged Administration Office

## Slide 28
Schuylkill Valley High School / DAO
Existing Conditions
EDUCATIONAL PROGRAM IMPROVEMENTS:
Additional Support Classrooms
Additional Divided Support Classrooms
Additional Conference /Seminar / S.G.I.
Additional S.E. / Gifted Classroom
Student Commons / L.G.I.
Enlarged Kitchen Area

## Slide 29
Schuylkill Valley SD Feasibility Study
Option Profiles Considered
Option 1
Option 2
Option 3
New
Intermediate
School
Middle
School
High
School
--
4-5
--
9-12
9-12
7-12
5-8
6-8
4-6
Elementary
School
K-4
K-3
K-3
(Status Quo)

## Slide 30
Schuylkill Valley SD Feasibility Study
Options
1
OPTION

## Slide 31
Schuylkill Valley SD Feasibility Study
Options
1
OPTION
Elementary School
FIRST FLOOR
SECOND FLOOR
Design for 1000-1125 Students
New Gym
Optional

## Slide 32
Schuylkill Valley SD Feasibility Study
Options
1
OPTION
Middle School
FIRST FLOOR
SECOND FLOOR
Design for 800-900 Students

## Slide 33
Schuylkill Valley SD Feasibility Study
Options
1
OPTION
High School
FIRST FLOOR
SECOND FLOOR
Design for 800-900 Students

## Slide 34
Schuylkill Valley SD Feasibility Study
Options
2
OPTION

## Slide 35
Schuylkill Valley SD Feasibility Study
Options
2
OPTION
Elementary School
FIRST FLOOR
SECOND FLOOR
Design for 800-900 Students

## Slide 36
Schuylkill Valley SD Feasibility Study
Options
2
OPTION
New Intermediate School
Design for 400-450 Students

## Slide 37
Schuylkill Valley SD Feasibility Study
Options
2
OPTION
Middle School
FIRST FLOOR
SECOND FLOOR
Design for 600-675 Students

## Slide 38
Schuylkill Valley SD Feasibility Study
Options
2
OPTION
High School
FIRST FLOOR
SECOND FLOOR
Design for 800-900 Students

## Slide 39
Schuylkill Valley SD Feasibility Study
Options
3
OPTION

## Slide 40
Schuylkill Valley SD Feasibility Study
Options
3
OPTION
Elementary School
FIRST FLOOR
SECOND FLOOR
Design for 800-900 Students

## Slide 41
Schuylkill Valley SD Feasibility Study
Options
3
OPTION
Middle School
FIRST FLOOR
SECOND FLOOR
Design for 600-675 Students

## Slide 42
Schuylkill Valley SD Feasibility Study
Options
3
OPTION
High School
FIRST FLOOR
SECOND FLOOR
Design for 1200-1350 Students

## Slide 43
Schuylkill Valley SD Feasibility Study
Option Comparison
Total Construction Cost
$51,199,800
Total Project Cost
$64,000,000
OPTION
2
OPTIONS
3
OPTION
1
E.S. building grade re-alignment to K-3 Elementary School
Recommended Alterations & Additions as required
M.S. building grade re-alignment to 4-6 Middle School
Recommended Alterations as required
H.S. building grade re-alignment to 7-8, 9-12 Jr./Sr. High School
Recommended Alterations & Additions as required
Maintain K-4 Schuylkill Valley Elementary School
Recommended Alterations & Additions as required
Maintain 5-8 Schuylkill Valley Middle School
Recommended Alterations & Additions as required
Maintain 9-12 Schuylkill Valley High School
Recommended Alterations & Additions as required
E.S. building grade re-alignment to K-3 Elementary School
Recommended Alterations & Additions as required
Construct New 4-5 Intermediate School Building
(Relocate 4th grade from E.S. & 5th grade from M.S.)
M.S. building grade re-alignment to 6-8 Middle School
Recommended Alterations as required
Maintain 9-12 Schuylkill Valley High School
Recommended Alterations & Additions as required
Total Construction Cost
$57,839,800
Total Project Cost
$72,300,000
Total Construction Cost
$52,799,800
Total Project Cost
$66,000,000

## Slide 44
5-8
$11.8M
$15M
Schuylkill Valley SD Feasibility Study
Option Comparison
OPTION
2
OPTIONS
3
OPTION
1
 | EST. CONST. COST | EST. TOTAL PROJ. COST
K-4 | $19.6M | $24.5M
5-8 | $12M | $15M
9-12 | $15.9M | $19.8M
SITE | $2.5M | $3.1M
SUB- TOTAL | $49.9M | $62.4M
CMC | $1.3M | $1.6M
TOTAL | $51.2M | $64M
*Total Project Cost Includes construction cost of building and site / plus financing fees, contingency fund, moveable furniture, commissioning fees, construction testing / inspections, fees for Topographic / Geotechnical surveys, A/E fees, permit fees detailed estimates, and utility fees, etc.
 | EST. CONST. COST | EST. TOTAL PROJ. COST
K-3 | $13.4M | $16.7M
4-5 | $18M | $22.5M
5-8 | $6.9M | $8.6M
9-12 | $15.9M | $19.8M
SITE | $2.5M | $3.1M
SUB TOTAL | $56.6M | $70.7M
CMC | $1.3M | $1.6M
TOTAL | $57.8M | $72.3M
 | EST. CONST. COST | EST. TOTAL PROJ. COST
K-3 | $13.4M | $16.7M
4-6 | $6.9M | $8.6M
7-12 | $28.8M | $36M
SITE | $2.5M | $3.1M
SUB TOTAL | $51.5M | $64.4M
CMC | $1.3M | $1.6M
TOTAL | $52.8M | $66M

## Slide 45
Schuylkill Valley SD Feasibility Study
Option Comparison
RECOMMENDED OPTION 1
PHASE 2
PHASE 1
$24M
ES Additions / Renovations
Totally renovate E.S. and add to accommodate
enrollment growth
High School
Selective infrastructure replacement due to
condition urgency (HVAC / Roofs)
After ES project is completed, evaluate enrollment growth for MS and HS at that time to determine the need for additions
Wait until next reimbursable periods for MS and HS renovations
  PDE allows reimbursement only one every 20 years
  MS and HS received last reimbursements almost 13-14 years ago – State reimbursements might be available in next 6-7 years from now
  Wait for moratorium to lift to receive reimbursements
Balance of work of higher rank at MS and HS to scheduled in a 5-10 year long range plan
$30M
$19.6M
$24.5M
$4.4M
$5.5M
Total Construction Cost Total Project Cost
Phase 1 Total:

## Slide 46
Schuylkill Valley SD Feasibility Study
Proposed Schedule
May 2020
School Board Authorizes Project Beginning
May / June 2020
Architect / Engineers Begin Production & Permits
September / October 2021
Bidding of Project
July / August 2023
Complete Construction / Move-In
(18-20 months maximum)
*Note: All governmental agency approvals must be in place before bid contract award; therefore, the target schedule is subject to length of agency review process.

## Slide 47
Schuylkill Valley SD Feasibility Study
Process / Contents of the Study
Demographic Review
(Student Enrollment, Population, Housing)
Facilities Study (Building Improvements & Construction Cost)
Educational Program Review
(Requirements / Needs)
Solutions (Construction Options)
Cost of Options
Schedule
Note: Study per PDE Requirements

## Slide 48
Schuylkill Valley School District
District-Wide Feasibility Study
7 March 2020